## Slide 1: ADXL367 Eval Software Quick Start Guide
Brock Bearss

## Slide 2: ADXL367 Eval Software Quick Start
Plot: XYZ Acceleration vs Samples
Register Settings Configuration
Register Map Snapshot
Click to update register map
Click to Start streaming data
Click to Stop streaming data
Not functional. Will be updated in future revision.
Perform hardware reset (5 sec)
Perform software reset
Exit program

## Slide 3: Device Overview Tab
On each tab, the Start Data Acquisition and Stop Data Acquisition buttons are the primary ways the user acquires data from the device.
Device Overview Tab
  View acceleration data, read the device memory map, and adjust device settings
The ADXL367 evaluation environment is divided into separate tabs, each of which specializes in commonly performed measurements for accelerometer devices.
  In this way, the evaluation system offers users an immediate ability to capture data for a wide variety of tests without the need to develop a customized hardware and software solution.
Additional functionality on this tab includes the ability to read the memory register or to take a snapshot of the current memory register values.
  Clicking the Read Register Map button gives a snapshot of the current memory register values, and it updates the serial number, device ID, part ID, and Rev ID.

## Slide 4: Demo Tab
Demo Tab
  Used to explore the various built-in modes that the ADXL367 offers
    Motion-activated Wakeup Mode
    Single/Double Tap Detection Mode
    Freefall Detection Mode
  Used to explore effect of modes on noise
    Ultralow power vs Ultralow noise mode comparison
    Wakeup mode enabled vs disabled noise comparison

## Slide 5: Data Record Tab
Data Record Tab
  Measure and record acceleration sampled at the selected output data rate
Data results are saved to a text file with the date, time, device ID, and serial number recorded as a header.
  Specify the file path by clicking the small folder icon under Directory to Save File and browsing to the desired folder
  If an existing file is selected, data is appended to the end of the file. The user can choose a data rate from 12.5 Hz to 400 Hz with the Data Rate Select control

## Slide 6: Extra Controls Tab
Extra Controls Tab
  Used to configure other register settings (additional to those found in the Device Overview tab)
Work in progress
  Some controls may not be implemented yet