## Slide 1: Low IMD3 Two-tone Signal Generation for ADC linearity Testing
Gunma University
Fumitaka Abe

## Slide 2: Outline
Research motivation
Low IMD3 two-tone signal generation
Experimental results
Applied to ADC testing（Under review）
Conclusion
Notes: This is the outline.
My talk consists of
・Research Motivation.
・Conventional Method
・Proposed Method
・Experimental Results
・Extension to ΔΣDAC
And ・Conclusion

## Slide 3: Outline
Research motivation
Low IMD3 two-tone signal generation
Experimental results
Applied to ADC testing（Under review）
Conclusion
Notes: This is the outline.
My talk consists of
・Research Motivation.
・Conventional Method
・Proposed Method
・Experimental Results
・Extension to ΔΣDAC
And ・Conclusion

## Slide 4: Research Motivation
Low distortion two-tone signal generation
for ADC testing with low cost AWG
by only changing DSP program
ADC
Conventional
DUT
Low quality test signal
IMD3
IMD3
AWG
ADC
Proposed
DUT
High quality test signal
IMD3
IMD3
AWG
DSP program
change

## Slide 5: Two-Tone Signal Generation with AWG
DAC
Digital
Signal
DSP
ADC
Y
DUT
AWG
High IMD3
Low quality test
IMD3
IMD3
IMD3
IMD3
Analog
Signal
Nonlinear
Nonlinear
Notes: This slide shows two-generation with AWG.
First of all we use two-tone test signal because communication application ADC receives narrow band signal.
AWG consists of DSP and DAC.
DSP generates digital signal Din and DAC converts it to analog signal Y.
The internal DAC of the AWG is Nonlinearity.
So, the output of the AWG includes high IMD3.
This is test signal for ADC.
The output of the ADC is here.
The IMD3 of the AWG is large compared with the ADC.
So, this is a low quality test.

## Slide 6: IMD3 is important for Two-tone Signal ！
Nonlinear Time Invariant System
Two-tone
signal
Hardly to remove with analog filter
IMD3
IMD3
Analog Filter
Notes: IMD3 is the most important component when f1 nearly equal f2 Two-tone Signal is input to the Nonlinearity System.
Because IMD3 is very close to fundamental wave f1 and f2.
So, we cannot remove this component with analog filter.
In the following slides I consider IMD3 is the dominant system.
That is third order Nonlinearity system.

## Slide 7: Outline
Research motivation
Low IMD3 two-tone signal generation
Experimental results
Applied to ADC testing（Under review）
Conclusion
Notes: This is the outline.
My talk consists of
・Research Motivation.
・Conventional Method
・Proposed Method
・Experimental Results
・Extension to ΔΣDAC
And ・Conclusion

## Slide 8: Conventional Test Signal with AWG
DAC
CLK
CLK
DSP
Analog Output
Digital Input
AWG
Nonlinear
Notes: Conventional test signal Din consists of only X.
X is this two-tone signal.

## Slide 9: IMD3 appear
IMD3 components appear
DAC
CLK
CLK
DSP
Analog Output
Digital Input
AWG
Nonlinear
IMD3
IMD3
Notes: The output of the DAC is here.
IMD3 components appear because of nonlinearity DAC.

## Slide 10: Proposed Test Signal with AWG
DAC
CLK
CLK
DSP
Analog Output
Digital Input
AWG
Nonlinear
Phase Switching Test Signal

## Slide 11: IMD3 disappear
DAC
CLK
CLK
DSP
Analog Output
Digital Input
AWG
Nonlinear
IMD3
IMD3
IMD3 are canceled
Switching Spurious appear
far from Signal

## Slide 12: Conv. and Prop. Two-tone Test Signal
Conventional
Proposed
Notes: f1 = 81,f2 = 131,fs = 4096

## Slide 13: Proposed Low IMD3 Two-tone Generation
- No hardware change
- No need for DAC nonlinearity identification
- No need for calibration
DAC
DSP
CLK
CLK
Nonlinear
DSP Program Change
AWG
Notes: I supposed four proposed technic to generate low IMD3 test signal.
We just only change the DSP program.
So, there is no need for hardware change, DAC nonlinearity identification, and calibration.

## Slide 14: Outline
Research motivation
Low IMD3 two-tone signal generation
Experimental results
Applied to ADC testing（Under review）
Conclusion
Notes: This is the outline.
My talk consists of
・Research Motivation.
・Conventional Method
・Proposed Method
・Experimental Results
・Extension to ΔΣDAC
And ・Conclusion

## Slide 15: Experimental Conditions
Spectrum analyzer
AWG
Agilent 33220A
ADVANTEST R3267
Signal
Frequency characteristic
1μHz~6MHz
Amplitude Resolution
14bits
50MSa/s
Maximum Sampling Rate
Frequency band
RBW
100Hz~8GHz
10Hz~30MHz
※ RBW : Resolution Band Width
Test Signal
Two-tone Signal
Sampling rate
Input Voltage
Offset
200kHz , 220kHz
10MSa/s
0.8~2.0Vpp (0.2Vstep)
0

## Slide 17: Outline
Research motivation
Low IMD3 two-tone signal generation
Experimental results
Applied to ADC testing（Under review）
Conclusion
Notes: This is the outline.
My talk consists of
・Research Motivation.
・Conventional Method
・Proposed Method
・Experimental Results
・Extension to ΔΣDAC
And ・Conclusion

## Slide 18: ADC Test System using Proposed Signal
Din
Aout
Ain
Dout
AWG
DAC
DSP
ADC
Nonlinear
3rd-order
Nonlinear
3rd-order

## Slide 19: ADC Test System using Proposed Signal
Din
Aout
Ain
Dout
AWG
DAC
DSP
ADC
Nonlinear
3rd-order
Nonlinear
3rd-order

## Slide 20: LPF
Din
Aout
Ain
Dout
AWG
DAC
DSP
ADC
Nonlinear
3rd-order
Nonlinear
3rd-order
LPF

## Slide 21: LPF
Din
Aout
Ain
Dout
AWG
DAC
DSP
ADC
Nonlinear
3rd-order
Nonlinear
3rd-order
LPF

## Slide 22: Phase Switching spurious Reducing ?
Nonlinear System
3rd-order
LPF
Phase Switching
Two-tone Signal
Conventional
Two-tone Signal
Nonlinear System
3rd-order
Nonlinear System
3rd-order
LPF
IMD3 level
IMD3 level

## Slide 23
Attenuation of Switching Spurious using LPF [dB]
IMD3 Error [%]

## Slide 24: Test System for ADC
AD7266
AD7265
12bits SAR ADC
EVAL-AD7266EDZ
EVAL-AD7266EDZ
EVAL-CED1Z
http://www.analog.com/jp/analog-to-digital-converters/ad-converters-ad7265
-products/EVAL-AD7265/evaluation-eb_AD7266_AD7265/fca.html
Evaluation Board
ADC
Converter Evaluation and
Development Board
PC
30,50kHz
Phase Switching
Two-tone Signal
AWG
Power
Supply
Notes: http://www.analog.com/jp/analog-to-digital-converters/ad-converters/ad7265/products/EVAL-AD7265/evaluation/eb_AD7266_AD7265/fca.html

## Slide 25: Outline
Research motivation
Low IMD3 two-tone signal generation
Experimental results
Applied to ADC testing（Under review）
Conclusion
Notes: This is the outline.
My talk consists of
・Research Motivation.
・Conventional Method
・Proposed Method
・Experimental Results
・Extension to ΔΣDAC
And ・Conclusion