## Slide 1: Hands-on Workshop: Buck Converter Basics
Presented by:
<<Presenter’s name>>
<<presenter’s title>>
Notes: 10/7/2018

## Slide 2: Outline
Buck Basics Lab Exercise
  Buck Converter Basics: Waveforms, PWM/Vin/Vout relationships
  Closing the Loop

## Slide 3: Buck Basics Lab Exercise
A wise old mechanical engineer, when presented with a 24-bit Analog to Digital converter, once said: “I want to understand this. Can I make a model out of one out of wood, on my lathe?”
In contrast, we CAN piece together a working buck converter from discrete parts.
Lab URL: https://wiki.analog.com/university/courses/electronics/buck_converter_basics
Materials Required:
  ADALP2000 Parts Kit
  ** OR **
  ADALM-BUCK-ARDZ board
  Arduino Uno (or compatible clone) and USB cable
Install LTspice
Install Arduino IDE
Recommend working in groups of 3
Print Out (slides with “Print Me” at the top):
  Pictorial and schematic, double-sided
  Data worksheets

## Slide 4: Alternative to an LDO for converting a high voltage to a low voltage:
This works, but let’s discuss output impedance, load regulation, efficiency… what do you think?
50% duty cycle square wave
RBC = Really Big Capacitor

## Slide 5: Let’s make one component substitution…
NOW we’re getting somewhere!
50% duty cycle square wave
RBC = Really Big Capacitor

## Slide 6: An Ideal-ish buck converter

## Slide 7: Inductor Value Selection
It’s a compromise:
Higher L = lower ripple current
  (Bigger is better!)
Lower L = smaller size
  (Smaller is better!)
Higher L = lower switching frequency, less switching loss
  (Bigger is better!)
Lower L = higher switching frequency, easier to filter
  (Smaller is better!)

## Slide 8
A buck converter we can build from scratch…

## Slide 9: Option 1: Breadboard Construction

## Slide 10: Option 1a: PermaProto construction

## Slide 11: Option 2: ADALM-BUCK-ARDZ
History Lesson: First workshop used hand-soldered modules.
Not practical long term, so we developed the ADALM-BUCK module
(Lab can also be done with breadboards, see Active Learning Wiki page)

## Slide 12: ADALM-BUCK connections (Prototype Rev.)
Select output capacitance
Inductance Selection: to pin 4,5,6,10,11,12)
Short to use ext. pulse
Switch Node probe conn.
Ext. pulse source
Ripple current sense
50 ohm load switch
Print Me!

## Slide 13: ADALM-BUCK schematic (Prototype Rev.)
Print Me!

## Slide 14: Probing Hints
The ADALM-BUCK board testpoints are designed for ADALM2000 leads, but standard scope probes are also usable.
Clip ground lead to TP1
For ripple current measurement - If you only have a two channel scope, connect CH1 to SW NODE top conductor, set DC coupling, trigger on rising edge, ~2.5V threshold. Set the other channel to AC coupling, and observe both sides of the RSENSE jumper. Convince yourself that most of the “wiggle” shows up at the lefthand (+) side. This is because the righthand side (-) has large bypass capacitors (install both jumpers.) Thus, the ripple current can be inferred from the wiggle at the lefthand side of RSENSE.

## Slide 15: Experiments:
REMOVE OSC OVRD jumper so that duty cycle is fixed 50%
Probe switch node
Probe RSENSE, set scope to AC coupled. Select different inductor taps, observe ripple
Probe downstream side of sense R, measure voltage ripple w/ 22uF, 47uF, 220uF output caps
These are not easy measurements:
  Trigger on CH2, switch node
  Turn on averaging

## Slide 16: Measurement Worksheet – Inductor Ripple Current
# of windings | Inductance (uH) (values measured on example board) | Ripple Current (mA p-p)
1 | 199 | 
2 | 841 | 
3 | 1997 | 
4 | 3730 | 
5 | 6020 | 
6 | 8810 | 
# of windings | Inductance (uH) | Calculated Ripple Current (mAp-p) | Measured Ripple Current (mA p-p)
1 | 199 | 210 | 150
2 | 841 | 51 | 43
3 | 1997 | 21 | 21
4 | 3730 | 12 | 15
5 | 6020 | 7.1 | 10
6 | 8810 | 4.9 | 9
Example data:
Print Me!

## Slide 17: Experiment: Output Ripple
Remove DC coupling jumper
Connect M2K 2-, 2+ across VOUT header
Install 10uF jumper only, Measure ripple current
Install 47uF jumper only, Measure ripple current

## Slide 18: Measurement Worksheet – Output Ripple
Output Capacitance | Ripple Voltage (mA p-p) 2 inductors | Ripple Voltage (mA p-p) 4 inductors
10uF |  | 
47uF |  | 
57uF |  | 
(Add external caps if you have some lying around) |  | 
Print Me!

## Slide 19: Closing the loop!
“load” the output with the 47-ohm resistor, note the “droop” in voltage
Upload Arduino sketch:
https://github.com/analogdevicesinc/Linduino/tree/master/LTSketchbook/Active Learning/LT1054_voltage_mode_buck_DC_ctrl
Install PWM control jumper
Connect downstream side of sense R to Arduino A0 (analog input)
Measure output, loaded and unloaded
See if you can catch a “transient dip”
Send “0”, “1”…”7”, “8”, “9”, “A” to set duty cycle to 10%-100% in 10% increments.
Send any other character to return to closed-loop operation.

## Slide 20: Terminal Setup
EITHER Arduino Serial Debug or TeraTerm will work
You may have several COM ports, trial and error
Set to 115200 Baud, 8N1
For TeraTerm, Run:
ttermpro.exe
For Arduino, click Serial Monitor icon

## Slide 21: Closing the Loop, Manual duty cycle control
Move jumper from “+RIIN-” to “OSC OVRD”
Install PWM control jumper
Connect downstream side of sense R to Arduino A0 (analog input)
Observe output voltage and duty cycle
Press “LOAD STEP” button, observe duty cycle
Send “0”, “1”…”7”, “8”, “9”, “A” to “open the loop” and set duty cycle to fixed 10%-100% in 10% increments. Observe output voltage.
Send any other character to return to closed-loop operation.

## Slide 22: Closed Loop Duty Cycle vs. load
Measure output, unloaded and loaded w/ 49.9 ohm resistor.
See if you can catch a “transient dip”
In serial terminal, note the “droop” in voltage, and corresponding increase in duty cycle to compensate

## Slide 23: Acknowledgements

## Slide 24
Thanks!