## Slide 1: ADALM SR-1
Corner Case Test Report

## Slide 2: Overview
Built for understanding the converter by examining both the power components, and the signal blocks that is normally not accessible in the controller IC.
VIN = 3-15V, IIN(lim) = 2A, Vout(max) = 22-24V
Rload = 6.25- 200 Ohm, with PWM for load step
Inductor, Capacitor and Load Resistor are adjustable
Adjustable frequency, and duty cycle.
Has option to operate in either Buck or Boost mode, with choice of either open-loop or close-loop operation.
Adjustable Current threshold, Feedback voltage, and Load control.
Tests are done in situation of possible misconfigurations from user. This is closely done with the activity of SR-1 at the web page. The tests for robustness are:
High Duty Operation for extreme values of Inductor
Different RLOAD test.
Thermal Check for Inductor and RLOAD
Start-up performance
Housekeeping circuit
Notes: So SR-1 was never meant to deliver the highest efficient around, nor the most accurate reading there is. But that is a good thing for this purpose because the user will know exactly how the flaws affects the circuit.

## Slide 3: Simplified Diagram and Component Selection
Inductance and Capacitance is larger than typical due to low switching frequency (20KHz on exercises) operation.
  Will cause large inductor current ripple especially at 7.7uH
  This large inductor current ripple will also limit (or change) our mode of operation.
  Other user might see a problem in operation if certain values are not configured properly, due to input current limit, or current threshold limit.
    Problem includes subharmonic oscillation, hiccup operation, or failure to regulate voltage.
  Capacitors are expected to be large due to low FSW.
Inductance Selection (P3) |  |  |  |  |  |  | 
Jumper |  |  |  |  |  |  | 
Position | EXT IND | 1 TAP | 2 TAPS | 3 TAPS | 4 TAPS | 5 TAPS | 6 TAPS
Function | Ext. inductor at TP3, TP4 | 7.7μH | 31.5μH | 72.6μH | 131.5μH | 216.2μH | 313.4μH
Output Capacitors Selection (4.7uF initial capacitance) |  | 
Jumper | P8, P11 | 
Position | Installed | Open
Function | P8 connect additional 47μF capacitance | No additional capacitance
 | P11 connect aditional 470μF capacitance | No additional capacitance

## Slide 4: Boost Converter: Open-Loop Max VOUT and Thermal Test VIN = 5V, FSW = 20KHz
L = 313.4uH (6 taps), RLOAD = 100 Ohms VOUT_measured = 15.2V Computed VOUT = 20.8V
L = 7.7uH
Same current threshold
Duty = 76%
Inductor showing sign of saturation.
Adjusting Duty Knob to determine maximum voltage possible
Tested beyond suggested duty value at minimum and maximum values of L.
CH1 | Vprot
CH2 | SW
CH3 | Vout
CH4 | IL
  At low L, over-current trips and no steady-switching occurs.
Vprot (yellow) also drops means that series FET turns off
Inductor heating up starts to reduce effective inductance; prone to saturation
OCP takes over instead of OTP
  At high L, max voltage is 15.2V Inductor operates at 91deg C.
Inductor operates at high inductor temp but still within specs (below 125deg C).
TIND = 91.68deg C
RLOAD = 60deg C
Notes: Computed value refers to the activity’s equation Vout = Vin(1/(1-D)) which does not consider any parasitics.

## Slide 5: Boost Converter: Max Duty Cycle Knob
RLOAD = 100Ohms
Max Duty Knob makes the Inductor to heat up to 230deg before shutting down with OTP
Hiccup occurs around 100deg but temp continues to drop.
OCP takes over that prevents SR-1 from starting up since Duty Knob is still maxed out and so, there is high input current.
After test, inductor is still functional, and the output voltage is within expected range at typical application.
Overtemperature Protection prevents inductor from staying at such high temperature. But temperature still overshoots due to limitation of sensing.
PLACE A DROP OF THICK CYANOACRYLATE GLUE BETWEEN SENSOR AND INDUCTOR
CH1 | Vprot
CH2 | SW
CH3 | Vout
CH4 | IL
During Max Duty Knob
Audible ringing occurs
Temp sensor
Inductor
TIND = 233.75 deg C
Place drop of glue here

## Slide 6: Boost Converter, VIN = 5V, FSW = 20KHz, RLOAD Test
RLOAD = 25 Ohm VOUT(max) = 8.2V
RLOAD = 50 Ohm VOUT(max) = 11.3V
Duty = 61.42% Computed VOUT = 13V
Duty = 72.22% Computed VOUT = 18V
A minute of prolonged exposure
Higher load heats the inductor greatly.
Increasing load (by adding parallel resistors) reduces the heat dissipated in each individual resistors.
Prolonged exposure shows sign of saturation at inductor current.
Inductor @ 93deg, RLOAD @ 51deg
Inductor @ 87deg, RLOAD @ 62deg
CH1 | Vprot
CH2 | SW
CH3 | Vout
CH4 | IL

## Slide 7: Explanation: Limitation of Output Boost Voltage
Inductor of SR-1
Additional factors that limits Boost Factor: 1. Drop of diode
2. FET’s RDSON 3. Series RSENSE
At higher RL , the Boost factor is greatly reduced.
Boost Factor
RL = Inductor ESR
R = Load resistor
V = Output Voltage
Vg = Input Voltage
Notes: This graph is from Erickson’s book. It shows here that boosting is limited by the ratio of inductor’s ESR and Load. The larger the RL , the small its boosting capability, and might even fail to boost.

## Slide 8: Beyond 50% Duty: Subharmonic Oscillation
VIN = 5V, FSW = 20KHz, L = 313.4uH
RLOAD = 25 Ohm VOUT = 7.5V
20KHz switching
Subharmonic oscillation
Due to operation without slope compensation especially at higher load current/high duty.
Current threshold allowed is too high.
Inductor not following Volt-Second Balance
Voltage EA
Voltage-to-PWM
Inner loop for Current
Switch Logic (Before Driver)
No Slope Compensation Ckt.
CH1 | Vprot
CH2 | SW
CH3 | Vout
CH4 | IL

## Slide 9: Subharmonic Oscillation (Boost)
Duty below 50%
Duty above 50%
Inductor current follows voltage-second balance every cycle. Inductor current value is the same at start and end of every cycle.
Inductor current rise every cycle and thus contains subharmonic oscillation that produces low-frequency oscillation.
CH1 | Vprot
CH2 | SW
CH3 | Vsense
CH4 | IL
CH1 | Vprot
CH2 | SW
CH3 | Vsense
CH4 | IL
Inductor not following Volt-Second Balance
Steady-state @ volt-second balance
Analog Devices ©2021 Analog Devices, Inc. All rights reserved.

## Slide 10: Closed-loop Operation
Device shuts down
Since board is initially unpopulated,
User might accidentally try to operate at Closed-loop operation with feedback being unpopulated.
CH1 | Vprot
CH2 | SW
CH3 | Vout
CH4 | IL
SR-1 shuts down in an event like this to protect itself
No further test are done for closed-loop operation
OCP asserted
Hiccup occurs
Notes: Closed-loop is not complete yet with bare-boards

## Slide 11: Buck Converter, VIN = 14.5V, FSW = 20KHz, RLOAD = 100 Ohm
L = 313.4uH VOUT(max) = 12.4 V
L = 7.7uH VOUT(max) = 8.67 V
Duty = 85.2%
Computed VOUT = 12.3
Mode of Operation turns DCM: VOUT does not follow the ideal CCM voltage conversion ratio.
Inductor peak and Input current is still within reasonable range
Oscillation due to switching.
Does not scale up when inductor current and duty got larger.
Tind @ 33deg, RLOAD @ 48deg
Tind @ 33deg, RLOAD @ 34deg
Input Current
Tind is same at L= 7.7uH because Current Threshold limits the peak current.
Ind. current
CH1 | Vprot
CH2 | SW
CH3 | Vout
CH4 | IL
Temperature Sensor
Prone to heating up
Load = 12.5 Ohm
Load = 100 Ohm

## Slide 12: Load Test and Thermal Performance
RLOAD = 12.5 Ohm VOUT(max) = 12V
RLOAD = 50 Ohm VOUT(max) = 13.4V
RLOAD = 25 Ohm VOUT(max) = 12.9V
Duty = 94.8%
Duty = 94.83%
Duty = 94.78%
Minimum off-time is around 5% of 20KHz
Waveform @ 25, 50Ohm is the same for RLOAD at 12.5Ohm.
OTP goes into hiccup after some time (when RLOAD Temp < 50deg)
The inductor is not as stressed as does in Boost Converter for the given loads. But it is still prone on reaching OTP for heavier load.
RLOAD has the highest temperature across the board. Some resistors are far from sensor.
Hiccup is 3.65s
VIN = 14.5V, FSW = 20KHz, L = 313.4uH
Tind @ 50.4deg, RLOAD @ 134.3deg
Tind @ 37deg, RLOAD @ 65deg
Tind @ 32deg, RLOAD @ 71deg
CH1 | Vprot
CH2 | SW
CH3 | Vout
CH4 | IL
Notes: Add thermal

## Slide 13: Boost Start up
Has 2 seconds delay from Vin power up.
Noticeable overshoot on inductor current but it is below the input current limit.
Startup Switching also occurs at FSW (20KHz)
VIN = 5V, VOUT = 12V, Rload = 50 Ohm
Input current rush at Cout = 4.7uF + 47uF + 470uF
IIN ~= 500mA
CH1 | Vout
CH2 | SW
CH3 | Vprot
CH4 | IL
CH1 | Vout
CH2 | SW
CH3 | Vprot
CH4 | Iin
Vprot drop due to series FET and Rsense when IL pulls current

## Slide 14: Buck Start-up
Switching delayed by 2.1 seconds.
Switching starts at set FSW
VIN = 12.5V
Rload = 6.25 Ohm
Start-up Duty is same as SS Duty
No large current overshoot

## Slide 15: Housekeeping Circuit
Input UVP – 3V
Input OVP > 14.5V
Current Limit > 2A RVP –> -40V
Main Components:
LTC4368 - 100V UV/OV and Reverse Protection Controller with Bidirectional Circuit Breaker Monitors input OVP, reverse protection, and input current limit.
LTC2912 - Single UV/OV Voltage Monitor Monitors temperatures, Output OVP. Will only turn on after USB_PWR is connected.
LT1017 - Micropower Dual Comparator

## Slide 16: Input Voltage Protection
Input OVP
Input Voltage rises to 15V.
Vp_prot is the voltage after the series FET (Converter Input).
Inductor current reduces to 0.
Vp_prot falls when switching stopped.
Converter initiated another start-up (2s delay) after restoring to nominal voltage level.
Input UVLO
Input Voltage falls to 3V.
Switching stop at 3V
Inductor current decay to 0.
No apparent issue on turn off.
CH2 | SW
CH3 | Vprot
CH4 | Vin
CH1 | Vout
CH2 | SW
CH3 | Vprot
CH4 | IL
CH2 | SW
CH3 | Vin
CH4 | IL

## Slide 17: Reverse Input Voltage Protection
Reverse Voltage Protection
Input voltage goes to -5V.
Input current remains relatively zero.
Vp_prot has no voltage, which indicates that the series FET is open.
No switching occurs
RVP at -15V
This will happen if user accidentally reversed at maximum input voltage
RVP protects SR-1 and no current flows to the rest of circuit
CH1 | Vin
CH2 | SW
CH3 | Vprot
CH4 | Iin
CH1 | Vin
CH2 | SW
CH3 | Vprot
CH4 | Iin

## Slide 18: Output OVP
Output OVP is set at 22V.
Hiccup occurs every 2 seconds.
Input current peak at 1.52A. (Below OCP) during start-up.
Output OVP occurs at Boost Mode. With no load, at high duty cycle setting.
CH1 | Vout
CH2 | SW
CH3 | Vin
CH4 | IL

## Slide 19: Conclusion
ADALM SR-1 provides an excellent initial experience for user to learn typical circuits for a Switch-Mode Power Supplies.
Performance is far from typical PMIC especially at extreme cases, but it is emphasizing the effect of each parameter (such as losses, duty cycle limit) and other typical circuit blocks.
  User will have no problem to work on its typical application.
  Intermediate topic such as slope compensation (in Current-mode Control) and soft-start circuit (for start-up profile) could provide additional insights for next revisions.
Although SR-1 can protect itself against over-temperature, temperature overshoot still exists due to delay in sensed temperature and actual temperature of the devices. The most vulnerable component against temperature is the inductor for Boost and RLOAD for Buck.
SR-1 is tested on different fault and proves that it can tolerate possible misconfigurations from user, thanks to its robust housekeeping circuit.